## Slide 1: Trans Septal Puncture
Dr Sanchna Dev S
Dept of Cardiology
TDMC

## Slide 2: To be covered
Gross Anatomy
Fluoroscopic Anatomy
Echocardiographic Anatomy
Intracardiac Echo Anatomy

## Slide 3: Gross anatomy –anterior view

## Slide 4: Development of the atrial septum

## Slide 6
Fossa ovalis <— septum primum
Annulus ovalis <—septum secundum free edge

## Slide 8: History lesson

## Slide 9: History lesson
The technique of transseptal puncture (TSP) was developed by Ross, Braunwald, and Morrow in 1959 to allow direct measurement of left atrial (LA) pressure.

## Slide 11: Indications
Percutaneous balloon mitral valvuloplasty (PBMV)
Transcatheter mitral valve repair( MitraClip)
Mitral valve-in-valve implantation
Transcatheter MV replacement
Mitral paravalvular leak (PVL) repair
Pulmonary vein isolation (PVI)
Percutaneous LVAD – TandemHeart, transseptal extracorporeal membrane oxygenation
LAA closure –watchman device
Anterograde treatment of LV and AV disease – “ no access patients”
—>Transcatheter AV replacement …..balloon aortic valvuloplasty

## Slide 13: Other indications
hemodynamic assessment (LA -indirect by Swan-Ganz catheter), (transaortic gradient - mechanical aortic prosthesis)
Closure of PFO with long tunnel
Carotid artery stenting in pts with acutely angulated arch-branch vessels and those with Takayasu arteritis.
In rare occasions, transseptal access may provide an alternative route for coronary interventions in pts with no suitable peripheral access
balloon atrial septostomy is another indication for TSP in patients with severe pulmonary hypertension who do not respond to medical therapy or are awaiting lung transplantation
Transapical route

## Slide 14: Fluoroscopic guided transseptal puncture
Fluoroscopy antedates echocardiography
2D technique - so always at least 2 views are mandatory

## Slide 15: RA angiography to guide TSP
No longer performed unless there is gross structural abnormality of heart , skeleton

## Slide 16: Basics of septal puncture
Access the systemic venous system
Perform the septal puncture around the fossa ovalis
Place a catheter into the LA for further interventions

## Slide 17: Access
Right femoral vein – straight course to RA
Rarely –left femoral vein
Even jugular access is reported

## Slide 20: Drag
Three movements
1st – SVC to RA , slight movement to right
2nd – Over limbus, slight movement to right
3rd – abrupt movement medial (left)

## Slide 22: Equipment

## Slide 23: BRK -XS

## Slide 28: Transseptal puncture

## Slide 30
Aortic pulsations maybe palpable
Short sharp movement with the distance between hub of catheter and needle maintained
Ensure that needle in LA

## Slide 31: How do we know that the needle is in left atrium?
Colour of blood aspirated is bright red
Inject contrast
Pressure tracing is of the left atrium

## Slide 32
Withdraw the needle and advance the dilator
Place a wire in LA
SafeSept wire if available ( 120cm Nitinol guidewire with 0.014 “ diameter + sharp and floppy “ J tip”
Advance the Mullins catheter over the needle
Advance
Anticoagulation only after safe puncture

## Slide 33: Alternatives to septal puncture needle
Reverse end of 0.014 “
Use RFA (bovie cautery) to the hub of the septal puncture needle

## Slide 34: Potentially difficult patients
1.Distorted anatomy
Chest /spine deformity
CHD
Severe valve abnormalities
2.ASD closure device/patch
3.Floppy septum- lateral wall of LA
4. Previous TSP (fibrotic)

## Slide 35: Helpful tools in difficult puncture
Tattoo of the fossa ovalis by contrast medium injection (visualisation of FO tenting)
RA angiography
Antegrade LA angiography
ICE
TEE
RF ablation

## Slide 36: Site specific TSP
1.MV interventions
for central MR jet –posterior and slightly superior
Medial jet – higher
Lateral jets - lower
2. LAA closure– posterior TSP
3. PV interventions –anterior > posterior
4. LVAD – mid FO

## Slide 37: TEE guided TSP
Superior and inferior localization is seen best in the bicaval view (90)
anterior and posterior localization is seen best in the short-axis (30) and 4-chamber (0) views.
An x-plane view that displays both the bicaval and the short-axis view is extremely helpful in puncturing the IAS at the desired location

## Slide 38: Intracardiac Echocardiography(ICE) for TSP
In ICE-guided procedures, a phased-array intra- cardiac echocardiographic catheter is advanced to the right atrium and manipulated to identify the “home” view
The initial survey of the IAS is then performed; from the home view, a posterior tilt of the transducer and a clockwise rotation of the catheter bring the IAS and FO into view (septal view)
After successful TSP, ICE allows direct visualization of the needle tip and its relationship to the surrounding cardiac structures

## Slide 40: Fusion of different imaging modalities
TEE + fluoroscopy (echo navigator system)

## Slide 42: ICE
Adv
Identifies right atrial structures
Identifies fossa and aortic root at the same time
Not in the way of X-ray equipment
No obstruction of fluoro
Disadvantage
Small field of view
May move during manipulation of transseptal sheath

## Slide 44: Complications
Pericardial effusion/tamponade
RA and LA needle puncture
Aortic puncture /perforation
Air embolism/TIA
Persistent ASD
Transient ST elevation
Potentially fatal

## Slide 48: Conclusion
Knowledge of the anatomy of IAS + Knowledge of associated structures
Safe and appropriate transseptal puncture

## Slide 49: Thank you

## Slide 50: Identify?
William Rashkind

## Slide 54: Intracardiac Echocardiography (ICE) is used to guide which of the following procedures ?
(i) Transseptal puncture (ii) Percutaneous closure of ASD (iii) Closure of PFO (iv) Electrophysiological procedures A:-(i) only B:-(ii) and (iii) only C:-(i), (ii) and (iii) only D:-All of the above

## Slide 55: Limbus of fossa ovalis derived from
septum primum
Septum secundum
Both
None
Ans :2