## Slide 1: CORONARY GUIDEWIRES
SRUTHI S PAL

## Slide 2: GUIDEWIRES
Guide wires are essential tools , to track through the vessels, allowing access and the ability to cross the lesions with interventional devices.
Simple spring type.
PTFE coated.

## Slide 3: Purpose
To track through the vessel
To access the lesion
To cross the lesion atraumatically
To provide support for interventional devices

## Slide 4: GUIDE WIRE MAIN CHARACTERISTICS
Torque control
Trackability
Steerability
Flexibility
Prolapse tendency
Radiopacity/visibility
Tactile feedback
Support

## Slide 5
GUIDE WIRE COMPONENTS
Coils
Covers
Coatings

## Slide 6: CORE
Inner part of guidewire.
Extends to proximal – distal part,where it begins to taper.

## Slide 7: Core Material

## Slide 9
CORE DIAMETER

## Slide 10: Core Taper

## Slide 12
TIP
Distal end of GW.
Tip style affect steering and tip softness.
Tip could be covered ;
a.Coils(spring tipGw)
b.Polymer(polymer tip Gw.

## Slide 13
TIP STYLE
Tapers distally to a variable extend .
Core to tip design(1 piece core ):Tapered core reaches the distal tip.
Shaping ribbon(2 piece core) : The core stops just before the distal end.
2 piece : easy shaping and durable shape memory.
1 piece : Better force transmission to tip and greater “tactile response” for operator.

## Slide 16
COILS

## Slide 17: Covers
Polymer or plastic
Provide lubricity
Smooth tracking through tortuosity

## Slide 18: COATINGS

## Slide 19: HYDROPHOBIC

## Slide 20: TIP LOAD
Force needed to bend a wire when exerted on a straight guide wire tip, at 1 cm from the tip
Floppy <0.5 g
Balanced 0.5-0.9g
Extra support >0.9g

## Slide 23: What is penetration power
Penetration Power = Tip Load/Tip Area
Penetration Power = Tip Load/ (∏ (D/2)2)

## Slide 24: Shapeability and shaping memory
Shapeability- allows to modify it's distal tip conformation
Shaping memory - ability of tip to return back to it's basal conformation after having been exposed to deformation and stress
Both do not necessarily go in parallel
Ss core wires-easier to shape

## Slide 26: COMPLICATION OF GW
Plaque embolization.
Arterial dissection and perforation.
Acute closure due to vasospasm.
Subintimal wire placement.
Wire fracture.

## Slide 27
Tip load of floppy wire
<0.5mg
>0.5mg
0.5mg
0.5-1 mg

## Slide 28
Wire for negotiating tortuous lesions
Hydrophobic
Hydrophilic
Floppy
Stainless steel

## Slide 29
Penetration power=
Tipload/Tip area
Tip load ×Tip area
Tip load + Tip area
Tip load – Tip area

## Slide 30: THANKYOU