## Slide 1: Hepatic Vein Doppler
Dr. Aiswarya Ravikrishnan

## Slide 2: Components of a Normal Multiphasic Spectral Doppler of Hepatic Veins
Normal waveform is triphasic / multiphasic, reflecting pressure changes in the right atrium (RA) transmitted to the hepatic veins.
S wave (systolic forward flow):
Blood flows from hepatic veins to RA during atrial relaxation + tricuspid descent in ventricular systole.
→ Normally dominant wave.
V trough:
Small dip after S wave; corresponds to end-systole/atrial overfilling.

## Slide 3
D wave (diastolic forward flow):
Blood flows into RA during early ventricular diastole (tricuspid opening, RA emptying).
A wave (atrial reversal):
Retrograde flow into hepatic veins during atrial contraction.

## Slide 4: Physiologic Factors Causing Artifacts in Hepatic Vein Doppler
Respiration
Inspiration → Increased forward flow (S, D waves more prominent).
Expiration → Reduced flow, more phasicity loss.
Patient position (supine vs. sitting).
Transducer angle / Doppler gain setting.
Valsalva maneuver → reduces venous return → dampens S & D.
Cardiac arrhythmias (e.g., AF) → irregular waveforms.
Normal anatomic variants (different vein orientation, smaller tributaries).

## Slide 5: Hepatic Vein Anatomy
Three major hepatic veins:
Right hepatic vein → drains right lobe.
Middle hepatic vein → drains medial segments (separates right & left lobes).
Left hepatic vein → drains left lobe.
→ Together, they divide the liver along cranio-caudal planes.

## Slide 6
Right inferior hepatic vein
Present in 30–60% of people.
Acts as an additional drainage channel for the right lobe.
Venous confluence pattern:
Left & middle hepatic veins often merge before entering the IVC.
This confluence is seen in 60–85% of individuals.

## Slide 8: Hemodynamics of Hepatic Vein Flow
Drainage:
Hepatic veins (HVs) drain into the right atrium (RA) via the inferior vena cava (IVC).
Correlation with RA pressure:
HV pressure and flow patterns mirror RA pressure changes.
This happens because pressure changes in the RA are transmitted directly to the HVs.

## Slide 9
Transmission characteristics:
Even with a well-developed Eustachian valve, RA pressure changes still pass clearly into the IVC and HVs.
The close proximity of HVs to the RA means pressure changes are transmitted without time delay.

## Slide 10
Effect of respiration:
HV Doppler waveforms also show respiratory variations in RA pressure.
Superiority over SVC study:
Compared to the superior vena cava, HV Doppler more clearly reflects RA pressure dynamics.

## Slide 12: How to Record Hepatic Vein Doppler (from Subcostal Long-Axis View)
Start with IVC long axis:
From the subcostal long-axis view, first visualize the IVC.
Identify hepatic veins:
With small probe adjustments, visualize hepatic veins draining into the IVC (most often middle and/or left HV).
Select the best HV:
Choose the HV that runs parallel to the ultrasound beam → this ensures accurate Doppler sampling.

## Slide 13
Optimize alignment:
Slight angulation of the transducer improves alignment with the vein’s long axis.
Sample volume placement:
Use a small sample volume (≈2 mm).
Place it inside the HV, away from the IVC junction to avoid contamination from IVC flow.
Avoid pitfalls:
If sample is too close to IVC → waveforms get distorted by IVC flow and can shift with respiration.
Excessive respiratory movement may also displace the sample volume out of the HV, giving poor signals.

## Slide 14
During apnea (no breathing movement):
Waveforms are cleaner and more stable.
Avoids respiratory artifacts and sample volume displacement.
Sweep speed:
50–100 mm/s: Best for analyzing waveform morphology (S, D, A reversal waves).
25 mm/s: Best for analyzing respiratory variation (because you capture more cardiac & respiratory cycles in one frame).
Apnea + fast sweep (50–100 mm/s) → fine detail of the wave.
Normal breathing + slow sweep (25 mm/s) → effect of respiration.

## Slide 17
Goal: Doppler beam should be parallel to hepatic vein (HV) flow for accurate waveform.
Step 1: Start with subcostal (subxiphoid) view → usually shows middle/left HV.
Step 2: If alignment poor → move probe from subxiphoid toward right midclavicular line → may improve middle HV alignment.
Step 3: If still poor → turn patient to left lateral position and repeat subxiphoid → right midclavicular approach.
Step 4: In obese patients → HVs may not be visible in subxiphoid or midclavicular windows.
Step 5: Try right axillary view (patient in left lateral position, probe marker toward feet) → may reveal right HV better aligned.

## Slide 18: Hepatic vein in Left Lateral Position in Axillary Line

## Slide 19: Hepatic vein in Right Midclavicular line

## Slide 20
Problem: From right midclavicular or right axillary views, the HV–IVC continuity may not be clear.
Solution: Differentiate HV from hepatic artery (HA) and portal vein (PV) using Doppler flow patterns:
Hepatic vein (HV): Flow away from transducer → shown below baseline (blue), multiphasic.
Portal vein (PV): Flow toward transducer → above baseline (red), monophasic, low velocity.
Hepatic artery (HA): Flow toward transducer → above baseline (red), pulsatile (high in systole, lower in diastole).

## Slide 21: Components of Normal Hepatic Vein Doppler Waveform
Systolic Forward Flow (S):
Flow towards RA during ventricular systole (because RA pressure falls as the atrium relaxes and empties into RV).
Usually a big single wave.
Sometimes split into S1 (early systolic descent of atrial base) and S2 (later systolic filling).
Systolic Reversal (SR):
Small reversal wave (above baseline) at the end of systole.
Caused by brief rise in RA pressure when tricuspid valve closes/ventricle contracts.

## Slide 22
Diastolic Forward Flow (D):
Forward flow into RA during ventricular diastole (when tricuspid valve opens and RA empties).
Usually second positive wave after S.
Diastolic Reversal (DR):
Small reversal after D-wave.
Due to transient rise in RA pressure at the end of rapid filling.
Atrial Reversal (AR):
Reversal wave during atrial contraction (end-diastole).
RA contraction pushes a little blood back into hepatic veins.

## Slide 23: Normal Hepatic vein Doppler waveforms

## Slide 24: Normal Hepatic vein Doppler waveforms

## Slide 26: Normal Hepatic Vein Doppler Physiology
Systolic vs Diastolic Forward Flow
S wave (systolic forward flow) is slightly larger than D wave under normal conditions.
Diastolic Reversal (DR)
Usually not prominent at normal HR.
Becomes more visible at slow heart rates (because filling phases are prolonged).
Effect of Respiration
Inspiration → forward flows (S & D) become stronger.
Expiration → reversal waves (SR, DR, AR) become more prominent.

## Slide 27: Normal Hepatic vein Doppler waveforms

## Slide 28: Hepatic Vein Doppler Waves & Corresponding Events
Atrial Contraction → AR (Atrial Reversal Wave)
When the RA contracts at end-diastole, blood is pushed backward briefly → small retrograde flow into IVC & hepatic vein.
RA Relaxation → S1 Wave (Forward Flow)
As the RA relaxes, pressure drops in RA → blood from hepatic vein flows forward into RA.
This produces the early systolic forward wave (S1).

## Slide 29
Tricuspid Valve Closure → Small Backflow Notch
When the tricuspid valve snaps shut, there is a brief rebound backflow into hepatic vein.
This separates S1 from S2.
Ventricular Systole (Tricuspid Annular Descent) → S2 Wave (Forward Flow)
During RV systole, the tricuspid valve ring is pulled downward toward the apex → enlarges RA cavity.
This creates suction and enhances forward flow from hepatic vein to RA → S2 wave.

## Slide 33
Systolic reversal (SR): Right atrial filling → backflow into hepatic vein.
Diastolic forward flow (D): Ventricular relaxation + tricuspid valve opening → right atrium empties into right ventricle → forward flow in hepatic vein.
Diastolic reversal wave: Right ventricle filling + tricuspid valve closure → transient backflow into hepatic vein.

## Slide 39: EFFECT OF RESPIRATION

## Slide 40: Inspiration
Inspiration → fall in intrathoracic pressure
In a normal pericardium, this pressure drop is transmitted to intrapericardial chambers.
Right atrial & right ventricular pressures fall.
Fall in RA pressure → increased venous return from IVC to RA.
Blood flow from hepatic vein (HV) to IVC increases.
Net effect:
Forward flow velocities ↑
Retrograde flow velocities ↓

## Slide 41: Expiration
Expiration → rise in intrathoracic pressure
Right atrial pressure increases
Flow from IVC to RA decreases
Forward flow in hepatic vein decreases
Slight increase in reversal velocities

## Slide 44
IVC obstruction (above HV junction):
Prevents normal inspiratory increase in blood flow to RA.
Hepatic vein obstruction:
Prevents inspiratory augmentation of flow from HV.
Reduced hepatic vein compliance (due to liver disease):
Seen in fatty infiltration, fibrosis (cirrhosis), tumors.
Leads to blunted flow variations and abnormal Doppler patterns.

## Slide 45: Obstruction

## Slide 46: AR wave abnormalities:
Atrial fibrillation- absent AR wave

## Slide 47: Tricuspid atresia - prominent AR

## Slide 48: Tricuspid Stenosis

## Slide 49: Factors affecting Systolic Foreward Flow

## Slide 50
Atrial fibrillation → no effective atrial contraction/relaxation → the atrial (AR) wave is lost on hepatic venous Doppler.
Right ventricular systolic dysfunction (from RV infarction, massive PE, or dilated RV cardiomyopathy) → the systolic forward wave (S wave) is reduced because the normal “downward pull” of the tricuspid annulus during RV contraction is weak.
Tricuspid regurgitation (TR) → during RV systole, blood leaks back into RA → extra volume in RA during systole → produces a large systolic reversal wave (SR) in hepatic vein Doppler.

## Slide 51: SYSTOLIC REVERSAL

## Slide 52: SYSTOLIC REVERSAL

## Slide 53: DIASTOLIC FORWARD FLOW

## Slide 54: CONSTRICTVE PERICARDITIS

## Slide 55
Normal: Inspiratory fall in intrathoracic pressure → transmitted to RV → RV accepts more venous return.
Constrictive pericarditis:
Inspiratory fall in pressure not transmitted to RV.
Inspiration: RV accommodates venous return by leftward shift of interventricular septum (IVS).
Expiration: IVS shifts right → RV filling restricted.
Venous blood backs up → expiratory diastolic flow reversal in IVC & hepatic veins.

## Slide 57: RCM

## Slide 59: COPD

## Slide 60: Positive Pressure Ventilation
Positive pressure ventilation → raises intrathoracic pressure
↑ Pressure on RA + intrathoracic IVC → ↑ back pressure on abdominal IVC & hepatic veins
Result: reduced forward flow in hepatic veins
Doppler changes:
Systolic & diastolic forward flow velocities ↓
Reversal waves mildly ↑

## Slide 62: Not true about Physiologic Factors Causing Artifacts in Hepatic Vein Doppler
Inspiration → decreases forward flow (S, D waves less prominent).
Patient position (supine vs. sitting) plays a role.
Transducer angle / Doppler gain setting can alter assessment.
Valsalva maneuver → reduces venous return → dampens S & D.

## Slide 63: Not true about Physiologic Factors Causing Artifacts in Hepatic Vein Doppler
Inspiration → decreases forward flow (S, D waves less prominent).
Patient position (supine vs. sitting) plays a role.
Transducer angle / Doppler gain setting can alter assessment.
Valsalva maneuver → reduces venous return → dampens S & D.

## Slide 64: Not true regarding recording hepatic vein Doppler
Slight angulation of the transducer improves alignment with the vein’s long axis.
Use a small sample volume (≈2 mm). Place it inside the HV, away from the IVC junction.
During apnea: Waveforms are cleaner and more stable.
Sweep speed: 25 mm/s: Best for analyzing waveform morphology (S, D, A reversal waves).

## Slide 65: Not true regarding recording hepatic vein Doppler
Slight angulation of the transducer improves alignment with the vein’s long axis.
Use a small sample volume (≈2 mm). Place it inside the HV, away from the IVC junction.
During apnea: Waveforms are cleaner and more stable.
Sweep speed: 25 mm/s: Best for analyzing waveform morphology (S, D, A reversal waves).

## Slide 66: False about Differentiating HV from hepatic artery (HA) and portal vein (PV) using Doppler flow patterns:
Hepatic vein (HV): Flow away from transducer → shown below baseline (blue), multiphasic.
Portal vein (PV): Flow toward transducer → above baseline (red), monophasic, low velocity.
Hepatic artery (HA): Flow away from transducer → below baseline (blue), pulsatile (high in systole, lower in diastole).

## Slide 67: False about Differentiating HV from hepatic artery (HA) and portal vein (PV) using Doppler flow patterns:
Hepatic vein (HV): Flow away from transducer → shown below baseline (blue), multiphasic.
Portal vein (PV): Flow toward transducer → above baseline (red), monophasic, low velocity.
Hepatic artery (HA): Flow away from transducer → below baseline (blue), pulsatile (high in systole, lower in diastole).

## Slide 69: ## 1. Basics
* **Technique:** Duplex Doppler US (intercostal / subcostal / transabdominal).
* **Normal anatomy:** Right, middle, and left hepatic veins → drain into retrohepatic IVC.
* **Display:** B‑mode + color Doppler + spectral tracing.
---

## Slide 70: ## 2. Normal Hepatic Vein Waveform
Although often described as *triphasic*, there are **four waves**:
* **A wave (retrograde):** atrial contraction → small reversal toward liver.
* **S wave (antegrade):** ventricular systole + tricuspid annular descent → dominant forward flow.
* **V wave (transitional):** atrial filling → may be antegrade, retrograde, or neutral.
* **D wave (antegrade):** passive flow during diastole (tricuspid opening).
👉 **Normal:** Multiphasic, with **S ≥ D**.

## Slide 71: ## 3. Factors Affecting Waveform
* **Respiration:**
* Quiet inspiration / end inspiration → triphasic.
* Valsalva / end expiration → blunted or monophasic.
* **Other influences:** ascites, pregnancy, peritonitis, mechanical ventilation.
* Exercise ↑ velocities but morphology preserved.

## Slide 72: ## 4. Systematic Analysis (Algorithm)
Ask four questions:
1. **Direction of flow?** Normal = hepatofugal. Reversal = obstruction (Budd–Chiari, compression).
2. **Regular or irregular?** Irregular → arrhythmia, turbulence, ventilation.
3. **Phasicity?** Multiphasic (normal) vs dampened/monophasic (cirrhosis, fatty liver, metastases, ↑ IAP).
4. **S vs D ratio?** Normally S ≥ D. If reversed (S < D) → right heart pathology.

## Slide 73: ## 5. Abnormal Patterns in Disease
* **Tricuspid Regurgitation:**
* Mild: S < D, still antegrade.
* Severe: S absent or reversed → retrograde.
* Often biphasic pattern (retrograde A/S/V vs antegrade D).
* **Right Heart Failure:** Similar to TR; S wave blunted, S/D reversed.
* **Constrictive Pericarditis:** Extra retrograde wave between D and A.
* **Cirrhosis / Fatty Liver / Metastases:** Dampened or monophasic.
* **Budd–Chiari / Obstruction:** Reversed or absent flow.

## Slide 74: ## 6. Special Situations
* **Liver Transplant:**
* Triphasic waveform → rules out stenosis/rejection (high negative predictive value).
* Blunted waveform → nonspecific (may be edema, rejection, cholangitis, fibrosis).
* **Pregnancy:** Temporary blunting; usually normalizes postpartum.

## Slide 75: ## 7. Key Take‑Home
* Normal HV Doppler is multiphasic with dominant S wave.
* Waveform = interplay of cardiac physiology + hepatic compliance + intra‑abdominal pressure.
* Abnormal patterns help differentiate **cardiac vs hepatic vs obstructive causes**.
* Use a **systematic algorithm**: Direction → Regularity → Phasicity → S/D ratio.